Inline Static Mixer:					Rapid Mix:

Flowmeter:						Streaming Current Monitor:

Gate Valves:						Globe Valves:

Check Valves:

Centrifugal Pump:							         Several Pumps:

Vertical Turbine Pump/Can:

Ground Level Tanks:			Standpipe:			Plan View:

Elevated Tanks:

Reservoir:				Plan View:				Baffled:

Well:		River/Creek:                                  Spring or raw water reservoir:

Cartridge Filter:

Pressure Tank:

60° Tube Settlers:					Distribution System:

Parallel Plate Settlers:                                              Generic Treatment Plant:

Flocculation Basin (single and two stage):

Pressure Gage:

Note:  All symbols should be labeled on schematics as shown in the following examples.

Water System Schematic

Water System Schematic

# Text boxes

11,725-gal Clearwell

(c. 1973)

FM

To Distribution

CL2, pH, Temp

20 Hp, 200 gpm pumps

26,785-gal Clearwell (c. 2002)

(both springs are captured as surface water)

SRC-AA

SRC-AB		   SRC-AC

Graham

Creek			        Spring #1		  Spring #2

NTU (1720D)

PAC

(PASS-C)

Static mixer

FM

Upflow Clarifier

floc basins

NTU

NTU (1720E)

NTU

Train #2

0.288 MGD

SCM

Train #1

0.288 MGD

(1990)

Soda Ash

Surface Scatter 6 (NTU)

Static mixer

Intake Pump Station

NTU (1720D)

Flowmeter

(Total flow and gpm)

Downflow Filter

Hypochlorite

Raw water sample tap

SRC-BE

SRC-BD

SRC-BC

SRC-BB

SRC-BA

Res #1

0.317 MG

Clearwell

WTP-A

SRC-AA

WTP-B

EP-B

EP-A

14” Bridge St Main

9 Services

14” Main

S. Yamhill River

Res #4

“Ballston Reservoir”

1.5 MG

Res #3

1.83 MG

Res #2

0.5 MG

Stoney Mt. Spring Sources

(Approx. 9 miles from Res #2)

From pump station

to the water

treatment plant                                          60-inch screening

pump station                       manhole                 South Yamhill River

wet well                                                              71-in x 47-in corrugated

metal pipe diversion

FM

FM

Variable Speed

floc basins

South Yamhill River

F-

NTU

NTU

NTU

Plant #1 – 0.5 MGD

(1982)

32.5% flow

Plant #2 – 0.8 MGD

(1990)

Soda Ash

Alum

(Potential Soda Ash)

Inline mixer

Intake Pump Station

67.5% flow

Splitter Box

Flowmeter

Tube Settlers

Filter

Res #1

0.25 MG

Hypochlorite

KMnO4 (taste & odor)

Construction of Kegbine Springs #1 and #2

(Similar for Both)

Concrete casing with collection holes at the bottom

Topsoil

Plastic Barrier

Rock

To Upper Collection Box

Construction of Big La Toutena Mary Spring

Concrete structure with metal roof, bolted hatch.  Water flows up

through rock in the bottom.

Topsoil

Rock

To Main Collection Box

Construction of Little La Toutena Mary Spring

Subsurface perforated piping under plastic barrier captures water

Topsoil

Plastic Barrier

Rock

To Main Collection Box

FM

SCM

1 MG Reservoir

SCM

Settling

Basin

NALCO 8105

Flocculation

Filter

1,900 gallon

Clearwell

Two 175-gpm pumps

Sodium Hypochlorite

42,000

gallon

Reservoir

Distribution

Bypass Line with valves (normally closed)

Well #10

Pringle Spring

Lafayette Springs Area

Well #3

(disconnected)

Blue Bird Spring

Well #8

Well #1

500,000 gallon reservoir

Well #2

City Park Well

(Chlorination/ pressure sand filtration for Fe/Mn removal)

●    EP C

●     EP D

Dayton/Lafayette Wellfield

● EP A

Well  #7

(emergency)

●   EP B

pH

Cl

●    Flow meter

Sodium hypochlorite

Soda ash

Test building

WTP-A