SAMPLE – Developed by Columbia County Rider

Wheelchair Lift Maintenance Policy

It is the intent of Columbia County Rider by way of this policy, to assure that our wheelchair lifts and ramps are maintained to the specifications prescribed by the device manufacturer. The maintenance of wheelchair loading apparatus will be performed by a combination of bus operators, mechanics and certified manufacturer technicians, depending on the level of service required. Services such as daily safety checks, monthly safety checks, and 10 cycle (daily) maintenance shall be performed by the bus operator and documented on the daily vehicle check sheet. All other maintenance and inspection shall be done by a qualified mechanic except those services where the manufacturer requires the service to be performed by a certified or authorized technician.

Wheelchair lifts shall be serviced based on duty cycles. A duty cycle is one full cycle from stowed position back to stowed position. The number of cycles a lift is operated in a given shift will be documented on the daily run sheet. There will also be a lift counter installed to use for verification in each vehicle. The supervisor will keep a running tally of the lift cycles for each vehicle, and send the vehicle in for the next designated service prior to reaching the maximum number of lift cycles allowed between services.

There are three different maintenance schedules for Columbia County Rider wheelchair lifts/ramps, described below; Schedule A, Schedule B and Schedule C. These maintenance schedules will be listed on the fleet maintenance spreadsheets using the appropriate schedule for the type of lift in that particular vehicle. Bus operators will do the 10 cycle inspection each day during their morning vehicle check and anytime during a shift where the lift is cycled more than 10 times. The 10 cycle inspection is described in the Schedule B attachment. In addition to this:

Schedule A includes inspection and service at 750, 1500 and 4500 cycles with service and inspection at consecutive 750 cycles.

Schedule B includes inspection and service every 150 cycles, with additional services required at 1800 cycles. This schedule also requires service at 3600 cycles to be performed by a certified technician.

Schedule C is applicable only to manual wheelchair ramps and requires a monthly safety check which includes cleaning and light lubrication of pivot points and hinges. Services within this schedule may be performed by the bus operator.

Lift Maintenance Schedule A - Braun

Braun 10 Cycles

| Overall condition | Listen for abnormal noises as lift operates: (e.g., grinding or binding noises) |
| --- | --- |
| Control Pendant | Verify that control pendant is undamaged and cable connector is tight. |
| Threshold warning system | Verify that system properly detects objects in threshold area and actuates the audible alarm. |
| Bridge plate load sensor | Verify that sensor inhibits downward movement of platform when a weight is present of lowered bridge plate. |
| Hydraulic fluids | Check for obvious hydraulic leaks |

Braun 750 Cycles

| Inboard roll stop hinge | Apply light oil - See Lubrication Diagram |
| --- | --- |
| Platform hinges (2) | Apply light oil - See Lubrication Diagram |
| Outboard roll stop clevis pin pivot points (4) | Apply light oil - See Lubrication Diagram |
| Outboard roll stop pin roller bearings (2) | Apply light oil - See Lubrication Diagram |
| outboard roll stop foot bearings (2) | Apply light oil - See Lubrication Diagram |
| Outboard roll stop arm slots (2) | Apply light grease - See Lubrication Diagram |
| Lift-Tite™ latches tower pivot points (2 latches-2 points) | Apply light oil - See Lubrication Diagram |
| Lift-Tite™ latch gas (dampening) spring pivot points (2 springs-4 points) | Apply light oil - See Lubrication Diagram |
| Inspect Lift-Tite™ latches and gas speings for wear or damage (bent, deformed or misaligned), positive securement (external snap rings) and proper operation. | Re-secure, replace damaged parts or otherwise correct as needed. Note: Apply light Grease to Lift-Tite™ latch tower pivot point if replacing latch. |
| Inspect inboard and outboard roll stops for proper operation | Correct or replace damaged parts. |
| Inspect outboard roll stop foot pivot for proper operation, positive securement and detached or missing spring. | Correct or replace damaged parts and/or lubricate. See Lubrication Diagram |
| Platform turnbuckle pivot points (2 turnbuckles-4 points) | Apply light oil - See Lubrication Diagram |
| Inspect lift for wear, damage or any abnormal condition | Correct as needed |
| Inspect for rattles | Correct as needed |
| Adjust fold pressure and outer barrier fold pressure (if applicable) | See applicable service manual |

Braun Consecutive 750 Cycle Intervals

Repeat all previously listed inspections, lubrication and maintenance procedures at 750 cycle intervals.

Braun 1500 Cycles

Perform all procedures listed in previous section

| Upper/lower fold arms (2) | Apply grease (synthetic) to contact areas between upper/lower fold arms. See lubrication diagram |
| --- | --- |
| Platform pivot pin bearings (4) | Apply light oil - See Lubrication Diagram |
| Platform fold axles (2) | Apply light oil - See Lubrication Diagram |
| Inboard roll stop lever bearings (2) | Apply light oil - See Lubrication Diagram |
| Inboard roll stop lever upper slots (2) | Apply light oil - See Lubrication Diagram |
| Saddle support bearings (8) | Apply light oil - See Lubrication Diagram |
| Parallel arm pivot bearings (8) | Apply light oil - See Lubrication Diagram |
| Handrail pivot pin bearings (4) | Apply light oil - See Lubrication Diagram |
| Hydraulic cylinder bushings (8) | Apply light oil - See Lubrication Diagram |
| Inspect inboard roll stop for: |  |
| Wear or damage | Re-secure, replace or correct as needed. See Platform Angle instructions and Microswitch Adjustment Instructions. |
| Proper operation. Roll stop should just rest on top surface of the base plate. |  |
| Positive securement (both ends) |  |
| Inspect handrail components for wear or damage, and for proper operation | Replace damaged parts |
| Inspect microswitches for securement and proper adjustment | Re-secure, replace or adjust as needed. See Microswitch Adjustment Instructions |
| Make sure lift operates smoothly | Realign towers and verticle arms. Lubricate or correct as needed. |
| Inspect outboard roll stop clevis pin securement set screws | Re-secure or replace (apply Loctite 217). |
| Inspect external snap rings: |  |
| * Platform slide/rotate pivot pins (2 per pin) | Re-secure or replace as needed. |
| Platform fold axles (1 per axle) |  |
| Inboard roll stop lever bracket pins (1 per pin) |  |
| Lift-Tite™ latch gas (dampening)spring (2 per spring) |  |
| Outboard rolls top clevis pins(1 per pin) |  |
| Outboard roll stop foot pins (2) |  |

Braun 1500 Cycles (Continued):

| Platform pivot pins (2) |  |
| --- | --- |
| Inspect platform fold axles and bearings for wear or damage and positive securement | Replace damaged parts and re-secure as needed. Apply Light Oil. |
| Inspect turnbuckle assemblies for wear or damage, proper operation and positive securement | Re-secure, replace or correct as needed. Apply light oil |
| Remove pump module cover and inspect: |  |
| Hydraulic hoses, fittings and connections for wear or leaks | Re-secure, replace or correct as needed. |
| Harness cables, wires, terminals and connections for securement or damage |  |
| Relays, fuses, circuit breakers and power switch for securement or damage |  |

Braun 4500 Cycles

Perform all procedures listed in previous section

| Inspect cotter pins on platform pivot pins (2) | Re-secure, replace or correct as needed. |
| --- | --- |
| Hydraulic Fluid (Pump) - check level Note: Fluid should be changed if there is visible contamination. Inspect the hydraulic system (cylinder, hoses, fitting, seals, etc) for leaks if fluid level is low. | Use Braun 32840-QT hydraulic fluid (Exxon® Univis HVI 26). Do not mix with Dextron III or other hydraulic fluids. Check fluid level with platform lowered fully. Fill to maximum fluid level indicated on reservoir (specified on decal). Do not overfill. If fluid level decal is not present - measure 35 mm from the fill port to locate fluid level. |
| Inspect cyclinders, fitting and hydraulic connections for wear, damage or leaks | Tighten, repair or replace if needed. |
| Inspect parallel arm pivot pin mounting bolts (8) | Replace if needed. |
| Inspect platform pivot pin, bearings and vertical arms for wear, damage and positive securement | Replace damaged parts and Re-secure as needed. Apply Light Grease during reassembly procedures. |
| Inspect upper/lower fold arms, saddle, saddle support and associated pivot pins, bushings, and bearings for visible wear or damage. | Replace if needed. |
| Inspect gas springs (cylinders) for wear or damage, proper operation and positive securement | Tighten, replace or correct as needed |
| Inspect saddle bearings (buttons-4) | Apply Door-Ease or replace if needed. See Lubrication Diagram. |
| Inspect vertical arm plastic covers | Re-secure or replace as needed. |
| Inspect power cable | Re-secure, repair or replace as needed. |
| Mounting | Check to see that the lift is securely anchored to the vehicle and there are no loose bolts, broken welds or stress fractures |
| Decals and Anti-skid | Replace decals if worn, missing or illegible. Replace anti-skid if worn or missing. |

Lift Maintenance Schedule B - Ricon

Ricon 10 Cycles

| Over all condition | Listen for abnormal noises as lift operates: (ie grinding or binding noises) |
| --- | --- |
| Control Pendant | Verify that control pendant is undamaged and cable connector is tight. |
| Threshold warning system | Verify that system properly detects objects in threshold area and actuates the audible alarm. |
| Bridge plate load sensor | Verify that sensor inhibits downward movement of platform when a weight is present of lowered bridge plate. |
| Hydraulic fluids | Check for obvious hydraulic leaks |

Ricon 150 Cycles

| Electrical Wiring | Inspect electrical wiring for frayed wires, loose connectors, etc. |
| --- | --- |
| Vehicle interlock | Place vehicle in non-interlock mode and verify that lift does not operate. |
| Decals | Verify that lift decals are properly affixed, clearly visible and legible. Replace if necessary. |
| Armrests | Verify that armrest fasteners are properly tightened. |
| Lift mounting points | Verify that vehicle mounting and support points are undamaged |
|  | Verify that mounting bolts are sufficiently tight and free of corrosion |
| Main lifting pivots | Verify that link pins on arms are properly installed, free from damage, and locked in position |
| Platform pivot points | Verify that platform moves freely, without binding and does not wobble |
| Bridge plate | Verify that bridge plate operates without binding during lift functions |
|  | Verify that bridge plate deploys fully when platform stops at floor level |
|  | Verify that bridge plate rests flat against base plate. |
| Front rollstop | Verify that rollstop is opened completely when platform is at ground level |
|  | Verify that rollstop closes and locks when platform leaves ground |

Ricon 150 Cycles (Continued):

| Hydraulic Power unit | CAUTION |
| --- | --- |
|  | Check and add fluid when platform is at ground level. Fluid that is added when platform is raised will overflow when platform is lowered. |
|  | Verify that pump hydraulic fluid level is at FULL mark when platform is at ground level |
|  | Add Texaco 01554 Aircraft Hydraulic Oil or equivalent U.S. mil spec H5606G fluid |
|  | Verify there are no hydraulic fluid leaks |
|  | Verify that manual backup pump operates properly |

Ricon 1800 Cycles

| Cleaning and lubrication |  |
| --- | --- |
|  | 1. Clean lift with mild soap and water and wipe dry. Prevent rust by coating all surfaces with a light weight oil. Remove excess oil. |
|  | 2. Spray penetrating oil (Curtisol ® Red Grease 88167 or WD-40 ®) where specified following directions on container. Remove excess grease from surrounding areas. |

Ricon 3600 Cycles

|  | CAUTION! |
| --- | --- |
|  | A Ricon authorized dealer must perform the following safety check. |
| Hydraulic cylinder hoses and fittings | Check hydraulic cylinder for evidence of leaks |
|  | Inspect hydraulic hoses for damage |
|  | Verify that all fittings are tight |
| Lift Maintenance Schedule C - Ramp |  |
| DAILY |  |
| Removable passenger seat | Be certain that removable passenger seat base is properly locked in position |
| Foldaway middle seat | Be certain that folding seat is locked firmly in position (either folded or unfolded) |

Ricon 3600 Cycles (Continued):

| MONTHLY |  |
| --- | --- |
| Sliding door | Wash lower door tracks and lightly lubricate contact surfaces |
| Folding ramp | Clean and light lubricate pivot points and hinges |
| SIX MONTH |  |
| Removable Passenger seat | Verify that locking mechanism on removable passenger seat operates properly by removing and reinstalling seat. |
| Electrical Connections (under hood) | Be certain that circuit breaker connections are free of corrosion; clean and apply protective coating as required. |
| ANNUAL |  |
| Under Carriage | Be certain undercoating is intact. Re-coat areas as required. Note: The rust inhibiting coating should provide years of trouble free service. However, severe condition (frequent use on unimproved or heavily salted road surfaces, etc) may cause premature corrosion. Any area where undercoating is bulging due to flaky rust should be cleaned using a wire brush, treated with primer and re-coated. |
| Hoses and fittings | Be certain that all fuel lines are intact and not damaged. Be certain that fuel fill hoses are free of cracking and damage. |