## Slide 1: Welcome ~
PUBLIC MEETING:
Beach Action Value and
Bacteria Standards Meeting

## Slide 2: Staff:
Aron Borok, DEQ – Water Quality Standards Specialist
Tara Chetock, OHA-OBMP – Program Coordinator
Curtis Cude, OHA-OBMP – Program Manager
Thomas Lossen, DEQ/OBMP – Natural Resource Specialist
Debra Sturdevant, DEQ – Standards and Assessments Manager
DEQ: Department of Environmental Quality
OHA: Oregon Health Authority - OBMP: Oregon Beach Monitoring Program
Notes: Introduce Staff
Purpose of meeting

## Slide 3
Notes: Summarize the flow of this evening’s public meeting

## Slide 4: New Beach Action Value
Oregon Beach Monitoring Program

## Slide 5: History:
1986
2000
2004
EPA Bacteria Standard
BEACH Act
Est. OBMP
Notes: 1986: EPA came up with health based bacteria standard and expected states to implement it
Coastal recreation waters defined as: The Great Lakes and marine coastal waters (including coastal estuaries) for swimming, bathing, surfing, or similar water contact activities
2000: Oregon and 20 other states did not adopt water quality criteria as protective as EPA’s bacteria standard, so EPA amended the CWA and required adoption of these standards by 2004. Amendment came under The Beaches Environmental Assessment and Coast Health (BEACH) Act of 2000.
  Est. funding and uniform criteria for testing, monitoring, and public notification
    Current criteria based on 50 yrs of epidemiological studies and outbreak investigations linking swimming in polluted water with adverse health effects
2004: All coastal and great lake states (30), territories (5), tribes (3) required to adopt beach water quality criteria for pathogens and pathogen indicators no later than April 2004; OBMP started monitoring in 2004. (38 total grantees)

## Slide 6: Sampling:
Infection
Exposure (bacteria)
Illness
Notes: OBMP samples for enterococcus, which is an indicator of fecal bacteria. Enterococci are bacteria that are present in the intestinal tract of warm-blooded animals, including humans, and have been found to indicate the presence of other bacteria that can make you sick.
Illness occurs from exposure to bacteria (direct contact, ingestion, inhalation, or open wound) – some exposures result in infection, which causes us to get sick.
Illness vary in symptoms and severity based on various exposures & host-pathogen interactions.
Common illness: gastrointestinal, respiratory, skin rash, ear, eye and wound infections.

## Slide 7: Sampling:
Method
Quanti- Tray
Estimates
colony forming units (100mL)
Unit
Most probable number (MPN)
Notes: MPN stands for most probable number.
Estimates the number of colony forming units (of bacteria) in 100mL sample of water.

## Slide 8: Recreational Water Quality Standard:
< 158 MPN
Advisory Level
BAV
* Most Probable Number
* Beach Action Value
Notes: Water samples over 158 MPN trigger a health advisory, this is also the same at the beach action value. The terms (advisory level and BAV) can be interchanged

## Slide 9
Sample
> 158 MPN ?
Resample w/in 96 hours
Resample
< 158 MPN?
NO
Issue Advisory
YES
Lift Advisory!
Resume Schedule
YES
Advisories:
NO
Continue Resampling
Notes: Sample exceeds 158 MPN = health advisory at sampled beach
Beach is not CLOSED; avoid water contact
Even though an advisory may not be in place, there may still be freshwater exceedences of the standard. OBMP suggests people stay out of streams flowing to the beach and the surf near these streams, especially during heavy rain events.

## Slide 10: Advisory Notification:
ADVISORY
BEACH SIGN
EMAIL PRESS RELEASE
HOTLINE
WEBSITE
WWW.HEALTHOREGON.ORG/BEACH
ADVISORY
NO ADVISORY
Notes: Contacts responsible party to flip advisory signs (OPRD, Local and City officials)
Notifies stakeholders and interested parties through email
Sends GovDelivery message to subscribers
  Communications group sends flash news message to media subscribers
Updates OBMP hot line (1-877-290-6767)
Updates OBMP website (www.healthoregon.org/beach)
Answers phone calls from interested parties
Performs media interviews as requested

## Slide 11: During an advisory:
YES
Fly kites
Walk/run/skip on beach
Picnics
Pictures/selfies
Whale watching
NO
Swimming
Surfing
Wading
Diving
Kayaking

## Slide 12: Program limitations
STRENGTHS
Collect water samples
Issue advisories
Identify data trends
Investigational sampling
Provide technical assistance
Outreach and education
WEAKNESS
Issue advisories for fresh water
Identify bacteria source
Regulate pollution
Illness reporting
Notes: Program limited by BEACH Act requirements.
Some limitations are:
Excludes “inland waters (upstream of a river/stream mouth having an unimpaired natural connection with the open sea)”
  Only “marine” water exceedences trigger an advisory
High bacteria levels in freshwater flowing to beach only used to indicate problems
Strategic with resources (funding is tenous)
  One program coordinator and one DEQ sampler
Beach illnesses often go unreported - symptoms occur after leaving/similar to other problems like food poisoning, sun exposure, etc.

## Slide 13: 2015 Monitoring:
Season
Memorial Day – Labor Day
Beaches Monitored
16
Sampling Locations
62
Notes: The Oregon Beach Monitoring Program (OBMP) monitors recreational water quality at ocean beaches. OBMP works with other state agencies to collect and test water samples, and when bacteria levels are above normal a water contact advisory is issued. The goal of the OBMP is to protect the public health by providing information about water quality, strengthening water quality standards at beaches, and promoting scientific research.

## Slide 14: 2015 Monitoring Schedule:
1
NORTH COAST
2
MID COAST
Rockaway, Twin Rocks, D River, Agate, Nye, Seal Rock
3
MID & SOUTH COAST
Agate, Nye, Seal Rock
Seaside, Cannon, Tolovana, Short Sand
Heceta, Bastendorff, Sunset Bay, Hubbard Creek, Harris, Mill
Notes: During the summer, ocean water is sampled on a three week rotating schedule on the priority ranking of the beach. The priority is determined by beach use, pollution hazards, previous monitoring results, and input from coastal stakeholders.
2015 sampling seasons changed somewhat from past years. Although OBMP continues to monitor the same number of beaches, the familiar north, mid and south coast sampling runs have changed slightly to accommodate resource constraints, while continuing to cover as much of the coast on a regular basis as possible. For the 2016 seasons, OBMP will repeat a three week sampling schedule, as shown on the slide. Once sampling is completed for weeks 1 through 3, the schedule will repeat until the sampling season ends.

## Slide 15: New Beach Action Value:
Who?
EPA – 2014 Recommendations
What?
Adopt BAV – 70 MPN
Justification
Where?
Coastal waters
Grantees under BEACH Act
Great lakes
Notes: 2014 – EPA National Beach Guidance and Required Performance Criteria for Grants
70 MPN – based on same water quality dist. as WQS; Single sample +70 MPN triggers advisory (Aron=WQS)
BAV is more conservative than WQS to meet EPA statuory requirement for public notifications of WQS exceedance (or likely exceedance) = protect of human health
Justification – (1) scientifically defensible (2) protect of primary recreation use

## Slide 16: New Beach Action Value:
When?
September 30, 2016
Why?
New study findings
How?
Resume 2015-16 schedule
2017 sampling season
Protect public’s health
Consider modifications
Notes: Studies – (pg. #10)
70’s – 80’s: study water of recreation water & health effects;
  found swimmers who recreate in contaminated fecal water = greater risk of GI illness than non-swimmers
  Swimming- assoc. G.I. increases as water quality degrades (measured by FIB)
2003-2010: (NEER) National Epidemiological and Env. Assess. Of Recreational Water
  Beaches freq. monitored w/ VERY low levels of FIB = risk of illness
  Increase Illness = increase bacteria
  qPCR - + assoc. w/ illness & bacteria levels
  QuantriTray – + assoc. BUT NOT statistically significant
  30-35 CFUs = significant increase of illness (WQS based on geometric mean w/ these values)
  Results informed 2012 RWQC that later support 2014 Guidance

## Slide 17: Possible Effects of New BAV:
New BAV
# of Advisories
Sample Schedule
???
Perceived Water Quality
Notes: 2016 sampling season – no change
BAV effects 2017 sampling season
Increase of advisories issued
  Perceived water quality
  Precipitation
Sampling Schedule
  Mirror 2015 -2016
  Modify as needed

## Slide 18: Data: 2010 – 2015
Chart: Number of Samples
Chart: 
| Number of samples exceeding 158 MPN | Number of samples exceeding 70 MPN
 | 88 | 206
Notes: Comparison of marine water samples collected over past five years.
70 MPN = 118 more exceedances (which is still more than current # of exceedances at 158 MPN)

## Slide 19: Advisories: 2015
Chart: 
| Seaside Beach | Cannon Beach | Tolovana Beach | Short Sands Beach | Rockaway Beach | Twin Rocks Beach | D River Beach | Agate Beach | Nye Beach | Seal Rock Beach | Heceta Beach | Bastendorff Beach | Sunset Bay | Hubbard Creek Beach | Harris Beach | Mill Beach
number of advisories at 158 MPN | 1 | 1 | 2
number of advisories at 70 MPN | 1 | 1 | 3 | 2 | 1 | 3 | 2
Notes: 2015 Advisory data only –
158 MPN = 4 Advisories
70 MPN = 13 Advisories
North = 1 (1)
Mid = 1 (6)
South = 2 (6)
Beaches with no advisories NOW have them (D River, Nye Beach, Bastendorff, Harris)

## Slide 20: Closer look: South Coast

## Slide 21
Chart: 
| Bastendorff Beach | Sunset Bay State Park Beach | Whiskey Run Beach | Bullards Beach | Face Rock State Scenic Viewpoint | Battle Rock State Park Beach | Port Point Beach | Hubbard Creek Beach | Ophir Beach | Nesika Beach | Gold Beach | Hunter Creek Beach | Meyers Beach | Harris Beach State Park | Mill Beach | Sporthaven Beach
Number of Advisories with BAV 158 | 1 | 8 | 0 | 0 | 0 | 1 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 6 | 4 | 0
Number of Hypothetical Advisories with BAV 70 | 4 | 22 | 0 | 0 | 0 | 1 | 0 | 8 | 0 | 0 | 0 | 0 | 0 | 17 | 8 | 1
Average Number of Swimmers Per Sample | 1.01 | 1.71 | 2.15 | 1 | 1.68 | 1.16 | 0.21 | 0.67 | 0.55 | 0.21 | 1.31 | 1.98 | 0.14 | 2
South Coast Data: 2010 – 2015
Notes: Advisory data from 2010 – 2015 for SOUTH COAST Beaches
Includes all beaches historically monitored for these years
158 MPN = 22 advisories
70 MPN =61 advisories
~ Almost three times more advisories with lower BAV
SPORTHAVEN, only beach with no advisories under current standard that would under new

## Slide 22: Closer look: Mid Coast

## Slide 23
Chart: 
| Roads End Beach | D River Beach | Nelscott Beach | Siletz Bay Beach | Gleneden Beach | Fogarty Creek Beach | Otter Rock Beach | Beverly Beach | Moolack Beach | Agate Beach | Nye Beach | Yaquina Bay | South Beach | Ona Beach | Seal Rock | Alsea River Beach | Governor Patterson Beach | Beachside State Park Beach | Yachats Wayside Beach | Neptune Beach | Heceta Beach | Florence North Jetty Beach | Umpqua Beach
Number of Advisories with BAV 158 | 0 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0 | 0 | 0 | 3 | 1 | 0 | 0 | 0 | 0 | 2 | 0 | 0
Number of Hypothetical Advisories with BAV 70 | 0 | 9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 9 | 0 | 0 | 0 | 7 | 1 | 0 | 0 | 0 | 0 | 4 | 0 | 0
Average Number of Swimmers Per Sample | 3.32 | 5.1 | 1.2 | 4.18 | 2.95 | 1.25 | 2 | 2.11 | 1.25 | 1.53 | 1.97 | 1.98 | 1.29 | 0.91 | 4.11 | 0.45 | 4.14 | 5.24 | 0.53 | 2.1 | 0.28 | 1
Mid Coast Data: 2010 – 2015
Notes: Advisory data from 2010 – 2015 for MID COAST Beaches
Includes all beaches historically monitored for these years
158 MPN – 11 advisories
70 MPN - 31 advisories
~ almost three times the advisories with lower BAV
Agate Beach only location with no advisories under 158 and one with 70

## Slide 24: Closer look: North Coast

## Slide 25
North Coast Data: 2010 – 2015
Chart: 
| Fort Stevens State Park Beach | Seaside Beach | Indian Beach at Ecola State Park | Cannon Beach | Tolovana State Park Beach | Hug Point State Park Beach | Short Sand Beach | Manzanita Beach | Nehalem Bay State Park Beach | Manhattan Beach State Park | Rockaway Beach | Twin Rocks Beach | Barview County Park Beach | Cape Mears Beach | Oceanside Beach State Wayside | Cape Lookout State Park Beach | Cape Kiwanda State Park Beach | Bob Straub State Park Beach | Neskowin Beach
Number of Advisories with BAV 158 | 0 | 4 | 1 | 5 | 3 | 1 | 3 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Number of Hypothetical Advisories with BAV 70 | 0 | 8 | 2 | 8 | 6 | 2 | 9 | 0 | 0 | 0 | 5 | 1 | 0 | 0 | 0 | 0 | 2 | 0 | 0
Average Number of Swimmers Per Sample | 7.28 | 8.49 | 6.36 | 7.66 | 6.65 | 2.97 | 4.98 | 5 | 1.85 | 1 | 1.99 | 1.64 | 0.46 | 3.64 | 4 | 4.62 | 2.75 | 4.04
Notes: Advisory data from 2010 – 2015 for NORTH COAST Beaches
Includes all beaches historically monitored for these years
158 MPN – 18 advisories
70 MPN - 43 advisories
Almost 2.5 times the number of advisories under lower BAV.
Cape Kwanda (2) and Twin Rocks (1) only beach with no current advisories; ONE under new BAV
High volume of swimmwers at beaches with more advisories

## Slide 26: Thank you! Questions???
OBMP Contact Information
Website: www.healthoregon.org/beach
Email: beach.health@state.or.us
Hotline: 877-290-6767

## Slide 27
OPEN PUBLIC COMMENT PERIOD
Beaches to be Monitored:
2017 – 2018 Seasons
… And we’re back!

## Slide 28: Adaptive Sampling Plan:
Monitored Beaches
2 years
Evaluate
Notes: As part of an adaptive sampling plan, the OBMP re-evaluates beaches and sampling locations every other year to ensure available resources best protect public health.

## Slide 29: Beach Evaluation Criteria:
Pollution Hazards
Historical Data
Candidate Beach
Beach Use
Public Input
Notes: The Oregon Beach Monitoring Program (OBMP) works with the Department of Environmental Quality (DEQ) to determine beaches that need monitoring based on several established criteria. These criteria include; pollution hazards present, previous monitoring data and test results, type and amount of beach use and public input.

## Slide 30: Proposed Schedule: 2017 – 2018
1
NORTH COAST
2
MID COAST
Rockaway, Twin Rocks, D River, Agate, Nye, Seal Rock
3
MID & SOUTH COAST
Agate, Nye, Seal Rock
Seaside, Cannon, Tolovana, Short Sand
Heceta, Bastendorff, Sunset Bay, Hubbard Creek, Harris, Mill
Notes: Mirrors sample schedule for the 2015 – 2016.
Rotate a three week schedule, starting Memorial Day to Labor Day.

## Slide 31: Comments???
OBMP Contact Information
Website: www.healthoregon.org/beach
Email: beach.health@state.or.us
Hotline: 877-290-6767